## Slide 1: prplMesh Controller

## Slide 2: Agenda
Overview
Components
Database
Tasks

## Slide 3: Overview
Certifiable EasyMesh MultiAP controller.
Single process task scheduler
Each task implements a MultiAP or Intel enhancement functionality
Message Router – Routes CMDUs Controller  Agent

## Slide 4: High-level Controller Architecture
PRPL mesh Controller
Master DB
Controller
DB Algo
SON Actions
Task Pool
Controller CLI
Controller
UDS
LAN Clients
Discovery
Load Balancer
Task
IRE Network
Optimization
Task
Client Steering
Task
Client Locating
Task
Statistics Polling
Task
Optimal Path
Task
Channel
selection
Task
BML
Task
BML Wifi
Credentials
Update Task
Association
Handling
Task
Service Fairness
Task
Persisted DB
Logger
Controller
Message Router
Health Check
Task
Multi
-
AP
Framework
Shared Library
'
s
BCL
TFL
BTL
BML
BML
=
BeeRocks Management Library
BTL
=
BeeRocks Transport Library
BCL
=
BeeRocks Common Library
Platform component
Thread
Process
BUS connection
TFL
=
TLV Factory Library
BeeRocks component
UDS
:
Unix Domain Socket
Sheared Library

## Slide 5: Database
Hierarchy of nodes based on network topology
Nodes represent network components
  APs, STAs, bridges, etc.
Updated by tasks or asynchronous events
Used by tasks for decision making and normal operation

## Slide 6: Database Node

## Slide 7: Database Hierarchies

## Slide 8: Tasks - Overview
Mechanism for performing background operations
Task pool – group of tasks
Task scheduling by the controller (son_master)
  Simple round robin scheduling scheme
Receive data through events from the controller
  Notifications / Responses
    CMDUs from agents
    BML requests

## Slide 9: Tasks
Task ID
  Task instance id
  Used for matching CMDU responses with tasks
Single instance tasks
  steering, optimal path (per client)
  client association
Multiple instance tasks
  steering, optimal path (multiple clients)

## Slide 10: Tasks
Task Pool APIs
  add_task(id)
  push_event(id, evtype, data)
  run_tasks()
Task APIs
  execute()
  work()
  handle_response()
  handle_response_timeout()
  handle_event()
  handle_event_timeout()

## Slide 11: Association Handling Task
Triggered on client association
Gathers client statistics
  RSSI, Capabilities (11V, 11K, etc) and store it in the DB.
Prevents jittering clients effect on network map
  Clients marked connected only after staying connected for some short time
Triggers Optimal Path Task upon success

## Slide 12: Optimal Path Task
Selects best AP for connected STAs
Triggered by
  Association handling task – on STA successful association
  AP Monitor – on RSSI threshold crossing
Triggers steering task based upon decision to steer
Dynamically detects single band clients.
Dynamically detect non 11k (legacy) clients.

## Slide 13: Optimal Path Task
Steering decision
    Based on maximum estimated downlink PHY rate (Default)
    Based on maximum estimated downlink RSSI
Estimated downlink PHY rate calculation using
  Number of antennas
  TX power
  Channel bandwidth
  Supported rates
  Downlink RSSI
    11K for supporting STAs
    Unconnected measurements
    Estimated uplink RSSI (same box)
Client Steering task is triggered if better target AP found

## Slide 14: Optimal Path Task

## Slide 15: Client Steering Task – Take from Tomer
Orchestrates client steering operation
Triggered by optimal path task
But also supports manual triggering from CLI
  Used for debugging, upper layer algorithm, etc.
Legacy steering
  Allow client (STA) in target AP
  Disallow in all other APs in the network
  After steering – allow client in all APs
    Prevents STAs from being locked out

## Slide 16: Client Steering Task

## Slide 17: Client Steering Task
802.11v Steering – BSS_TM_REQ
    For STAs supporting 802.11v
    STA marked non 11v if it didn’t respond 3 times in a row
      Legacy steering will be used for this STA
    3 times, it is considered legacy client.
    Imminent – Mandatory steering request
    Non-imminent – Optional steering request (STA may refuse)

## Slide 18: Client Steering Task
Two steering options available:
  1. Optional steering – used only for STAs that support 11v.
    The request is sent without any disassociate timer.
    If the STA rejects that request, the steering task is cancelled without any consequences.
  2. Forced steering – used for 11v clients and legacy clients.
  The request using a disassociate timer set to 10sec for 11k clients or set to 1sec for legacy clients (configurable).
  In addition, the controller will add the STA to blacklist on all APs except of the one it wants to steer to.

## Slide 19: Client Steering Task
    In case of forced steering, one of the following scenarios are possible:
    The STA accepts the request – and will be steered smoothly.
    The STA does not support 11v – and will be disconnected after 1sec, leaving it only single AP to connect to.
    The STA supports 11v but rejects the BSS request – and will be disconnected after 10sec leaving it only single AP to connect to.
    Dynamically detect 11v supported clients - according to respond to 11v.

## Slide 20: Client Locating Task
Wired (Ethernet) clients locating
Sends ARP query to all connected agents
Collects ARP responses
Client connected to deepest agent which answered
Updated clients triggers DB update and BML listeners (for network map)

## Slide 21: BML Task
Manages all BML connections to the controller
Registers/Unregisters listeners for network map and statistics updates
Sends updates to all listeners on network map changes or statistics events

## Slide 22: BML Wi-Fi Credential Update Task
Synchronizes credentials update between all agents
Triggered by BML request
Algorithm
  prepare – sends credentials to all agents
  pre-commit – all agents save new credentials in platform DB
  commit – all agents reset and start with new credentials
  Can be aborted if one of the slave did not respond

## Slide 23: BML Wi-Fi Credential Update Task