## Slide 1: PRPL mesh
Framework

## Slide 2
Framework components
The PRPL mesh framework consist of the following components:
Local bus and broker
1905 Transport
Discovery service
WFA_CA
Platform service
management service
Code location:
https://github.com/prplfoundation/prplMesh/tree/master/framework

## Slide 3: PRPL EasyMesh architecture
PRPL mesh Agent
Platform
Service
1905
.
1
Topology
&
discovery service
1905
.
1
Transport
service
OS
/
Distribution Management Entity
PRPL mesh Controller
BTL
BTL
Local Message Bus
(
XSub
-
XPub
)
PAL
TFL
TFL
BWL
Hostapd
Supplicant
Netlink
BML
TFL
WLAN Driver
(
cfg
80211
)
BML
–
BeeRocks Management Library
BTL
–
BeeRocks Transport Library
(
TX
/
RX CMDU
)
BWL
–
BeeRocks WLAN Library
D
-
WPAL
–
Dynamic WLAN Platform Library
Sheared
Library
TFL
–
TLV factory Library
PAL
–
Platform Abstraction Library
PPL
–
Platform Plugin Library
MPL
–
Management Plugin Library
PPL
Network Stack
L
2
–
Raw Socket
TFL
TFL
Management
Service
OS
/
Distribution
FAPI
D
-
WPAL
WLAN
API
Management
API
?
s
MPL
Algorithms
Algorithms
Features
Multi
-
AP Framework
Local BUS IPC
Legend
API
Framework
WLAN
Controller/agent

## Slide 4: PRPL mesh
Local bus

## Slide 5: Agenda
Overview
  Recap – PUB/SUB messaging
  Components
  Class Diagram
Example code

## Slide 6: Recap - PUB/SUB messaging
    PUB/SUB messaging - asynchronous service to service communication method
    Message - Starts with a Topic string (used for filtering)
    Subscriber
          Subscribes to one or more topics (filter incoming messages)
          Subscribing to an empty topic = subscribing to all messages
      Filtering - Longest prefix match
          Example: “abcdef” will match the “abc” topic

## Slide 7
Local bus - overview
Inter-node PUB/SUB bus
Connecting multiple subscribers to multiple publishers over a local broker
Acts as an abstraction layer for any PUB/SUB messaging library
  Currently supporting ZMQ and NNG
  Easy to support other libraries
Notes: Explain a bit on PUB/SUB and what is “topic” – topic is a longest prefix match of the message start string used by the PUB/SUB bus to pass messages to subscribers.
It is basically a “filter” for unwanted messages, that allows subscribers to receive only messages of interest

## Slide 8
Local bus - overview
Components
local_bus executable
Broker
shared library (mapfcommon.so)
Message, Poller, Socket
Broker Interface
Broker Config
Code location:
https://github.com/prplfoundation/prplMesh/tree/master/framework/common
Notes: Explain a bit on PUB/SUB and what is “topic” – topic is a longest prefix match of the message start string used by the PUB/SUB bus to pass messages to subscribers.
It is basically a “filter” for unwanted messages, that allows subscribers to receive only messages of interest

## Slide 9: Local bus – Broker
XSUB/XPUB proxy
  Multiple subscriber  multiple publisher
  Forwards messages – frontend  backend
Endpoints – frontend & backend
  Unique string (path name)
  Connects publishers and subscribers
  Used by underlying messaging library

## Slide 10
Local bus – Broker Config
Broker configuration class
Input - JSON configuration file
frontend and backend endpoints
Optional security
Shared by Broker and BrokerInterface classes
Default location: <install prefix>/share/local_bus.conf

## Slide 11
Local bus – Broker API
Init() – parse config and bind endpoints
Run() – start forwarding

## Slide 12: Local bus – Message
Any message sent over the local bus is either a message object or a derived message object
  Example: CmduMessage
Received messages are constructed using the factory design pattern (based on topic)

## Slide 13: Local bus – Message
Message structure
  Topic – message topic
  Header – message version (const), message total length (excluding topic & header)
  Frame/s – message data (blob)

## Slide 14: Local bus – Socket
Socket abstraction over msglib_socket (nng/zmq)
Motivation – replace underlying messaging library with any implementation supporting PUB/SUB
Base class – Socket
Derived classes – PubSocket, SubSocket

## Slide 15: Local bus – Socket API
PubSocket
  Send(message)
SubSocket
  Subscribe<message_type>()
  Subscribe(topic)
  Unsubscribe(topic)
  Receive()

## Slide 16: Local bus – Poller
Provides polling abstraction over msglib sockets and linux fds
Based on Linux polling (POLLIN / POLLERR / etc.)
Poller APIs
  Add/Modify/Remove(socket)
  Add/Modify/Remove(fd)
  Poll(timeout = -1)
  CheckEvent(socket)
  CheckEvent(fd)

## Slide 17: Local bus – Broker Interface
Used for communicating over the bus
Simple wrapper class which contains both a PUB and a SUB socket

## Slide 18: Local bus – Broker Interface
APIs
  Init() - connects both sockets to the bus based on config
    SubSocket connects to config.backend endpoint
    PubSocket connects to config.frontend endpoint
  subscriber() – subscriber socket getter, used for receive and poll
  publisher() – publisher socket getter, used for send

## Slide 19
Local bus – Class diagram

## Slide 20
Local bus – Example Code
Notes: Split to client – server

## Slide 21
Local bus – Example Code
Notes: Split to client – server

## Slide 22: PRPL mesh
1905 Transport

## Slide 23: Agenda
Overview
Features
Flow diagram
Components details

## Slide 24
1905 transport - overview
1905 transport is a process that provides a transport service for all entities that wish to send CMDUs outside of the box.
It is not based on the BBF code and was implemented from scratch.
The transport service solves the “MID generation sync issue”
(while we have both agent and controller on the same box).
Supports all EasyMesh features required by the standard.
Code location:
https://github.com/prplfoundation/prplMesh/tree/master/framework/transport

## Slide 25
1905 transport - features
Packet filtering, verification and sanity.
MID assignment
Fragmentation/ de-fragmentation
Duplication detection
Multicast relayed/non-relayed
Optional - Alternative transport to support reliability/security (TBD)

## Slide 26
1905 Transport flow diagram
Flow color map:
Received duplicate packet
Relayed multicast receive
Unicast receive
Unicast to other device
Multicast transmit
Alternative transport transmit (to other device)
Unicast to self (1905 or alt. transport).
Alternative transport transmit

## Slide 27
1905 transport - Main processing poll loop
A basic design decision for the 1905 Transport is to make it a single thread process with a single central dispatcher/poll loop.
The poll loop gets input from:
  Local bus – for outgoing packets (and control).
  Network interface sockets – for incoming packets.
  Network interface status
  Global bus (TBD)

## Slide 28
1905 transport - Packet sanity checking
Packet sanity is doing mimmal verfication of the packet.
It parse the headers and check for It is doing some mimimal validation for the packet like:
  Correct packet type (LLDP or 1905)
  Minimum size of packet.
  Consistent of End of Message TLV.
  Can be extended if needed..
Notes: TBD – look at the code and complete

## Slide 29
1905 transport - Bridge Configuration
The IEEE1905 standard defines unique behavior for bridging of the protocol's multicast packets.
The 1905 CMDU header contains a "relayIndicator" bit.
Only when this bit is set a packet should be forwarded by the bridge.
In order to support this requirement we:
  Modify the default bridge behavior such that it will drop 1905 multicast packets.
  Handle the packet forwarding in the transport service itself.
We use the following command to configure the bridge:
ebtables -t filter -I FORWARD 1 -p 0x893a --destination 01:80:c2:00:00:13 -j DROP

## Slide 30
1905 transport – Packet Relaying
Code with additional documentation details: https://github.com/prplfoundation/prplMesh/blob/master/framework/transport/ieee1905_transport/ieee1905_transport_packet_processing.cpp
Origin | Packet Type | Forward To |  | 
 |  | Local Bus | Bridge Interface | Individual Network Interfaces
Network | Unicast not to local device | Dropped by the Linux networking stack |  | 
Local Bus | Multicast | + | - | + (all)
Network | Multicast && relay==1 | + | - | + (all but originating i/f)
Network | Multicast && relay==0 | + | - | -
Local Bus | Unicast not to local device | - | + | -
Any | Unicast to local device | + | - | -

## Slide 31
1905 transport - Packet formatting and MID generation
MID as defined by EasyMesh standard should be unique incremental number per box (AL mac). This must be true for every request or notifications.
For responses MID should be the same as the request.
To meet requirement #1 - a single transport entity should allocate the MID.
  Problem: how will the agent/controller know if a response has the correct MID ?
  There is an option to add “cookie” to the message meta-data
  The transport will publish an Ieee1905TxConfirmationMessage with the cookie + the genrated MID.
  This is used by the controller to match the respond to the corresponding MID.
  TBD – we plan to move the implementation to the transport so that it will handle the mapping.

## Slide 32
1905 transport - Network Interfaces - Tracking of Status
The transport listen on the Local Bus for control packets.
These are used to configure the list of network interfaces which will be used by the 1905 Transport.
It holds a table of the relevant interfaces and a table for the bridge interfaces.
  The transport track interface status in the poller loop and mark them as active when a netlink event indicates it is UP && RUNNING.
                The interfaces from the table are used as explained in the packet relaying slide.
interface index | bridge interface index | active
11 | -1 | 1
4 | 5 | 0

## Slide 33
1905 transport - Network Interfaces - Packet Reception
Reception of packets is done using a dedicated raw socket per network interface.
Packets will be received whenever a POLLIN event is detected on a network interface fd.
The originating interface of a packet is important for forwarding relayed multicast packet.
(sent to all interfaces except the originating one).
The transport uses the socket filtering mechanism (based on BPF).
Using the filter only the following packets will be received:
  1905 and LLDP multicast
  1905 unicast to us - to either AL MAC or any interface MAC
The raw socket has a filter attached which does most of the filtering work in the linux networking stack.
The filter is generated using the following command:
tcpdump -dd '(ether proto 0x893a or ether proto 0x88cc)'

## Slide 34
1905 transport - Packet De-duplication
MID's of received packets (for a specific source address) are a monotonously rising number.
That is true, at least within a reasonable timeout - i.e. they can go back upon wrap-around event or when a device reboots.
We can safely assume that if two packets, with the same MID are received after minimal timeslot they are not duplicated.
This period should be long enough to allow for any buffered/in-transit duplicate packets to be flushed.
However, should be short enough to handle the case when a device reboots (and may reuse MID)
Internal data structure:
Key |  |  |  | Value
MAC Address | Frag ID | Message type | MID | Timestamp
9a:96:32:00:12:10 |  |  | 0x0010 | 
9a:96:32:00:13:40 |  |  | 0x2053 | 

## Slide 35
1905 transport – Fragmentation/De-fragmentation
When a CMDU is larger than a standard defined threshold (1500 bytes) it will be fregmanted.
Fregmantation is done by the TLV boundary, A TLV larger then the MTU will be dropped.
De-fragmentation of received packets will be done before publishing a CMDU on the local bus.
The fragments of multicast CMDU will be relayed as-is before de-fragmentation is complete.
The fragments of a CMDU are buffered until either:
  The complete CMDU is available.
  A certain timeout has elapsed (IEEE1905.1 does not specify the duration of this timeout)
Key |  |  | Value |  |  | 
MAC Address | Message type | MID | Last frag num | index (buf offset) | buf | timestamp
9a:96:32:00:12:10 |  | 0x0010 | 1 | ​ | * | 
9a:96:32:00:13:40 |  | 0x2053 | 0 | ​ | * | 

## Slide 36: 1905 transport – High level messaging flow

## Slide 37: PRPL mesh
1905 TLV factory

## Slide 38: Agenda
Overview
Motivation
Features
Examples

## Slide 39: Overview
Python package, generates C++ code to represent TLVs
Input – yaml configuration file, source path, output path, yamls path
Designed for TLV classes, but not limited to them
  Can generate any type of data element
Code Location:
https://github.com/prplfoundation/prplMesh/tree/master/framework/tlvf

## Slide 40: Motivation
Easy to read – simple representation for TLVs by yaml format
Easy to use – adding / modifying TLVs is easy by adding / modifying yaml file
Standardize the APIs provided by TLV classes
Single codebase for all TLV classes (easy to maintain)
Alternatives and why we didn’t use them
    Google protobuf – no control on byte stream order
    Facebook thrift – c++14, we have c++11
Notes: MultiAP defines multiple types of messages.
Each message is encapsulated within a 1905 cmdu and contains one or more TLVs .

## Slide 41: Features
Getter/setter for each TLV field
Fully serializable – no memory copies
Single reusable buffer
Allows static and dynamic size TLVs (dynamic list as a field)
Supports external structs to be used inside TLV

## Slide 42: Features
Support namespaces, constants, enums and structs
Support all C++ standard types and C++ strings
Support optional parameters (under development*)
Seamless endianness handling
Automatic length calculation

## Slide 43: IEEE1905 / MultiAP message
CMDU Header
TLV 1
…
TLV N
TLV End Of Message
Type
Length
AL MAC
Number of local interfaces
local interface 1
local interface 2
…
local interface N
Tlv example: “device information”
MAC address
Media type
Info length
Media specific information

## Slide 44: Yaml files
Yaml is a human-readable data serialization language.
All the classes, structs and enums are configured in yaml files and generated based on these configurations.
File attributes (namespace, includes, etc.)
Class name
Class attribute
Class members
Additional internal types

## Slide 45: Example generated .h file
File attributes
Class API
Class members
Internal types

## Slide 46: Non-generated (copied) source files
cBaseClass
  Base class for all the classes generated by the TLVF
  Holds the buffer and pointers (similar to sk_buff)
CmduMessageTx / CmduMessageRx
  Rx/Tx Descriptor
  holds the CMDU header and all TLV classes
swap.h
  Endianness conversion utilities
tlvfutils.h
  type conversions (e.g. mac_to_string())

## Slide 47: Tx Packet flow
Allocate tx_buffer
Construct and assign tx_buffer to a CmduMessageTx descriptor
Create CMDU header with CmduMessageTx::create()
  Optional: set values in CMDU header (relay, MID)
Add TLVs with CmduMessage::addClass()for each TLV
  Update TLVs data using class getters / setters
Notes: CmduMessageTx: Class that contains the buffer and manages the cmdu header class and all the TLVs.

## Slide 48: Tx Packet flow
Finalize before sending to the network with CmduMessageTx::finalize()
  Endianness conversion for the whole message to network byte order
  Adds End of Message TLV
Send the message buffer using CmduMessageTx::getMessageBuff()
Notes: CmduMessageTx: Class that contains the buffer and manages the cmdu header class and all the TLVs.

## Slide 49: Tx Packet flow
Notes: CmduMessageTx: Class that contains the buffer and manages the cmdu header class and all the TLVs.

## Slide 50: Rx Packet flow
Allocate rx_buffer
Receive packet data into rx_buffer
Construct and assign rx_buffer to a CmduMessageRx descriptor
Parse the CMDU header using CmduMessageRx::parse()
Add TLVs (based on message type) with CmduMessage::addClass()for each TLV
  Repeat until reaching End Of Message TLV
Notes: CmduMessageTx: Class that contains the buffer and manages the cmdu header class and all the TLVs.

## Slide 51: Rx Packet flow

## Slide 52: Configuration file options
include_yaml_path – path to yaml files
include_source_path – non-generated (copied) files
source_license_header – optional, path to license file
debug - debugging and logging options

## Slide 54: Running TLVF
tlvf.py <source files path> <yaml path> <output directory path> -c <configuration file path>
Options:
  --print-dependencies - prints the list of all yaml files read by the script
  --print-outputs - prints the list of generated and copied files

## Slide 55: TLVF - Backup

## Slide 56: Under the hood
Tlvf performs these steps:
Copy all non generated source path files to output dir
Load all yaml files to internal DB and process each file:
  Process the yaml file into python dictionary using PyYaml
  openObject – preparation - Generate code template based on the object type (class, struct, etc.)
  generateObject – Generate object specific code – class members, methods, etc.
  closeFile – write the generated code into .h and .cpp files

## Slide 57: Under the hood Markers
Tlvf uses markers in generated code to easily locate each code line location. for example: //~class_private_func_insert marks where to insert private methods code These markers are ignored when writing to the file and don’t appear in the output (can be changed by configuration for debug purposes).

## Slide 58: Under the hood Build optimization – ignore re-compiling files
Tlvf checks for differences when writing files.
If the output files already exists, it compares the file content to the generated code and only writes into the files in case there are differences.
That way the generated files are only touched when their content is changed.
It can be used for build optimizations so that this C++ code will not be compiled again.

## Slide 59: PRPL mesh
Discovery service

## Slide 60: Agenda
Overview
Flow diagram
Message handling

## Slide 61
Discovery service- overview
Discovery agent module is responsible for exchanging topology update messages in the network.
It has a database that contains all the information on the device and it‘s direct neighbors and provides an API for the agent to fetch the data.
Using this information the controller (which queries all agents) can build a full network topology map.
It interacts with multi AP agent and 1905 transport over local bus.
Code location:
https://github.com/prplfoundation/prplMesh/tree/master/framework/discovery_agent

## Slide 62
Discovery service- overview
Discovery agent support the following messages:
IEEE 802.1 bridge discovery:
A bridge discovery message is an LLDP packet used to find the nearest bridge
Using a special multicast address (01-80-C2-00-00-0E), which is not forwarded by the bridge.
2. Topology discovery protocol:
- Topology discovery message (neighbor multicast)
- IEEE 802.1 bridge discovery message (neighbor multicast)
- Topology query message (unicast)
- Topology response message (unicast)
Topology notification message (relayed multicast)
3. Higher Layer information protocol:
In addition to the topology discovery protocol, a 1905 management entity may discover additional
Higher Layer information using the Higher Layer query/response procedure with the following
messages:
- Higher Layer query message (unicast)
- Higher Layer response message (unicast)

## Slide 63
Discovery service- Multicast discovery procedure

## Slide 64
Discovery service- Topology query
Queries the collected information
Usually sent by Controller
Agent should reply with collected topology

## Slide 65
Discovery service- Topology notification

## Slide 66
Discovery service- Message handling
Message | Description | Action
wlan_ap_event | WLAN AP state change event | Update local database for WLAN AP list will be used in forming HL query response message
cl_assoc | Client association event | Update local database for associated client list will be used in forming HL query response message
CMDU_TOPL_QUERY_MSG | Topology query message | Prepare and send unicast topology response CMDU message on local bus
CMDU_TOPL_NOTIFY_MSG | Topology notification message | Update local database for neighbor list relayed multicast is handled by transport agent
CMDU_DISC_MSG | Topology discovery message | Update local database for neighbor list
ETH_P_LLDP | LLDP discovery message | Add/update local database for neighbor list, specifically set bridge existence as false for this neighbor
CMDU_HL_QUERY_MSG | Higher Layer query message | Prepare and send unicast HL response CMDU message on local bus
CMDU_IFSTAT_CHANGE_MSG | Interface state change message | Update local database for interface list, trigger topology discovery for interfaces added new

## Slide 67: PRPL mesh
WFA_CA

## Slide 68
WFA_CA overview
WFA_CA is used to control the agent for citification usage.
It listen on TCP socket and waits for CAPI commands from the WFA setup.
It implements the following CAPI commands:
CA_GET_VERSION - Return ca_version (agent version)
DEVICE_GET_INFO - Return vendor, model and version
DEV_RESET_DEFAULT - Reset the device to its default program specific configuration
DEV_SET_CONFIG - Set device configuration with given parameters.
DEV_GET_PARAMETER - Retrieve the requested parameter information (mac, bssid, Almac).
DEV_SEND_1905 - sending a 1905 message with the specified TLVs.
START_WPS_REGISTRATION
Code location:
https://github.com/prplfoundation/prplMesh/tree/master/framework/wfa_ca

## Slide 69: PRPL mesh
Platform service

## Slide 70
Platform service overview
Platform service is basically the platform manager that will be explained in the Agent’s slides which is currently part of the agent
Platform service today is not yet connected to the local bus
There is a planned task to move the “platform manager” from the agent and put it on the bus.
The Platform manager has plugin per OS/SDK called bpl.
More details on the platform manger are on the agent slides.

## Slide 71: PRPL mesh
Management service

## Slide 72
Management service overview
Management service today is not yet connected to the local bus – this is planned task.
Instead, we have a C library called BML to be linked by the orchestration of the OS.
The library is using UDS socket is sending requests to the controller which are routed to the BML task.
More details on the BML task and BML library are on the controller slides.